## Slide 1
Capstone Final Presentation
A Virtual Reality (VR)-based Brain-Computer Interface Development (CP12-DOE-193)
Academic Supervisor : Assoc. Prof. Denny Oetomo
Student members: Albert Tien Hann
Jiawei Liao
Harfiyanto Dharma Santoso

## Slide 2: Problem statement
Control virtual robot arm using classified brain signals to perform tasks in VR.
The robot arm needs to be able to pick up and place virtual objects on a table.
Notes: We want to use brain signals to control a virtual robotic arm to pick objects in VR

## Slide 3: Background and Motivation: Brain-Computer-Interface (BCI)
Scalp-Electroencephalogram (S-EEG) and other measures of brain activity provides non-muscular channels for the brain to communicate with the external world, forming what is known as brain-computer-interface (BCI).
S-EEG is
  Portable
  Non-invasive.

## Slide 4: Background and Motivation: Prevalence of paralysis
Neurological diseases such as:
brain injuries
Spinal cord injuries
impair patient to lose control of body muscles.
In severe cases, patients could be 'locked-in' and unable to communicate with the external world.
BCI systems could assist severely paralyzed patients with daily tasks: type letters, answer questions, give simple commands

## Slide 5: Background and Motivation: Virtual Reality (VR) and Augmented Reality (AR) BCI systems
Virtual Reality (VR) is an ideal asset of BCI systems
  A visually immersive user experience
  Easy to expand possible BCI applications.
Augmented Reality (AR) will be a potential viable component of BCI systems
  Real-life control of robots and smart appliances
  user interface transferred from VR BCI solutions
Oculus Rift VR goggles

## Slide 6: Project Roadmap

## Slide 7: Hardware and Software Setup: System Overview
Stage 1
Notes: Signals from different part of the brains are analysed using Matlab. The signals
How to wear VR headset and EEG cap together?
How to identify, eliminate or minimize Noise in signal?
What types of EEG signals to use as control?
How many control inputs needed for the robot to complete the task
How accurate should the control inputs be?
What robot type to simulate?
What Graphical User Interface layout is suitable in control the robot?

## Slide 8: Hardware and Software Setup: Hardware
1. Oculus Rift
2.g.GAMMAcap electrodes and cap
3. Unity VR application
4. g.USBAMP
Biosignal amplifier
5. Simulink EEG recording

## Slide 9
Fast Fourier Transfer
(FFT)
Brain signal voltage
BCI methods: Brain Signal Collection

## Slide 10: BCI methods: EEG electrodes positioning
Motor Imagery Multi Class Signals
Steady State Visually Evoked Potential (SSVEP)
Motor Cortex (Movement)
Occipital Lobe
(Vision)
Electrodes Positioning (International 10-20 System)

## Slide 11: BCI methods: Steady State Visually Evoked Potential (SSVEP)
3.5Hz - 75Hz visual stimulus can excite the retina to produce potential in the occipital lobe1 at the fundamental frequency and subsequent harmonics.
1 (Luis Fernando Nicolas-Alonso * and Jaime Gomez-Gil, Brain Computer Interfaces, a Review)
Blinking Box Stimuli
Resizing Box Stimuli
Chess-grid Box Stimuli
15Hz Sinusoidal light

## Slide 12: BCI methods: SSVEP Decoding Using Canonical Correlation Analysis
Canonical Correlation Analysis (CCA)1 was used to decode the SSVEP signal by comparing the correlation between raw signals and reference signals corresponding to each frequency stimuli.
A reference signal corresponding to a frequency stimuli is a series of sin and cos up to the nth harmonic.
i.e: two target classifier with two-harmonic reference
Sin(f)
cos(f)
sin(2f)
cos(2f)
Two Harmonic Reference Signal of frequency f
1 (Harold Hotelling. “Analysis of a complex of statistical variables into principal components.”In: Journal of educational psychology 24.6 (1933), p. 417.
Notes: david

## Slide 13: BCI methods: SSVEP Decoding Using Filter Bank Canonical Correlation Analysis (FBCCA)
Filter Bank Canonical Correlation Analysis (FBCCA)1 cuts SSVEP signal into several sub-bands to perform multiple CCA results and generate a weighted sum result to achieve increased accuracy.
i.e :
6 Band FBCCA
1 (Xiaogang Chen1, Yijun Wang2,3, Shangkai Gao1, Tzyy-Ping Jung2 and Xiaorong Gao1, Filter bank canonical correlation analysis for implementing a high-speed SSVEP-based brain–computer interface)
Entire Signal bandwidth
Useful bandwidth

## Slide 14: BCI methods: Best SSVEP Stimuli using FBCCA analysis
Human Subject #3
4 Chess Grid Box stimuli (9,11,13,15Hz)
Visually Comfortable
95%
Accuracy
5 Seconds processing window times

## Slide 15: BCI methods: Motor imagery of left/right hand squeeze
Left/right hand squeeze imagination task could be differentiated by assessing the Beta (12-30Hz) band power difference between C3 and C4 electrode using FCz as the reference.
5 Seconds processing window times
80%
Accuracy
Notes: david

## Slide 16: Task Design: Picking Up A Ball
Ball Spawn Area
Ball Randomly Spawns
Notes: Picking Up
Ball Spawn Randomly

## Slide 17: Task Design: Grid Navigation System
(Up, Down, Left, Right, Confirm)

## Slide 18: Task Design: Quadrant Navigation System
(Quadrant 1, 2, 3, 4, Back)

## Slide 19: Task: Picking Up A Ball Three Setups
Setup 1: (SSVEP MI Hybrid) + (Grid Navigation)
Setup 2: (SSVEP Only) + (Grid Navigation)
Setup 3: (SSVEP Only) + (Quadrant Navigation)
Navigation System
BCI
Methods
Steady State Visually Evoked Potential (SSVEP)
Motor Imagery (MI)
Quadrant Navigation System
Grid Navigation System

## Slide 20: Task: Picking Up A Ball Setup 1: SVEP MI Hybrid + Grid Navigation

## Slide 21: Task: Picking Up A Ball Setup 2: SSVEP + Grid Navigation

## Slide 22: Task: Picking Up A Ball Setup 3: SSVEP + Quadrant

## Slide 23
Task: Picking Up A Ball Best Performing Setup: SSVEP + Quadrant
Quadrant navigation system + SSVEP
Average Task Time: 58.867 seconds
Best Case Task Time: 20 seconds
83.33% Trial Success Rate

## Slide 24
Thank you!
Albert Tien Hann
Jiawei Liao
Harfiyanto Dharma Santoso